| Specification | www.chineseslipring.com |
| --- | --- |
| Basic Parameters: |  |
| Ring ring | Number1-10 | Option ● Operating speed ● Circuits ● Signal, power combined ●Current &Voltage ● Lead wire length ●Lead wire exit direction ● Protection class ● Connector |
| Operating Speed | 0-500rpm |  |
| Working Temperature | -40℃~ +80℃ |  |
| Working Humidity | 60%RH or higher |  |
| Electrical: |  |
| Voltage Rating | 240VAC/DC |  |
| Current Rating | 1A-3A |  |
| Dielectric Strength | ≥500 VAC@50Hz between per circuit |  |
| Insulation Resistance | 500 MΩ@500VDC |  |
| Electronic Noise | ≤7mΩ |  |
| Mechanical: |  |
| Contact Material | Gold on Goldl |  |
| Wire Size | AWG28 or AWG30 UL certification |  |
| Cable length | Standard 200mm (7.874inch) |  |
| Caps Materia | Plastic or metal |  |
| Moment | ≤ 0.15 g · m (only parameter to consider) |  |
| Protection Grade | IP54 or higher |  |
| Others: |  |

Pan-cake slip ring

While height is critical and there is no much limitation on outer diameter, and the working speed is not very high , normally, lower than 300rpm, Pan-cake slip ring is your best selection.